## Slide 1: Tính ổn định HTĐKTĐ gián đoạn 14th Lecture, 9th Dec 2023 3rd September 2023
Giảng viên/Instructor:
Trung tá, ThS. Nguyễn Ngọc Hưng
Email: hungtd@mta.edu.vn

## Slide 2: Mục đích, Yêu cầu
Mục đích
  Determine the input-output stability of a z-transfer function.
  Determine the asymptotic stability of a z-transfer function.
  Determine the internal stability of a digital feedback control system.
  Determine the stability of a z-polynomial using the Routh-Hurwitz criterion.
  Determine the stability of a z-polynomial using the Jury criterion.
  Determine the stable range of a parameter for a z-polynomial.
  Determine the closed-loop stability of a digital system using the Nyquist criterion.
  Determine the gain margin and phase margin of a digital system.
Yêu cầu
  Chú ý nghe giảng
  Làm lại các ví dụ và tự thực hiện các bài tập về nhà.
  Sử dụng máy tính và matlab để kiểm chứng lý thuyết

## Slide 3: Nội dung bài học
Khái niệm về tính ổn định
Mối quan hệ vị trí điểm cực và tính ổn định
Các điều kiện ổn định
Cách xác định tính ổn định hệ thống

## Slide 4: Nội dung bài học
Khái niệm về tính ổn định
Mối quan hệ vị trí điểm cực và tính ổn định
Các điều kiện ổn định
Cách xác định tính ổn định hệ thống

## Slide 5: Definitions of stability
Asymptotic stability
Marginal stability
Input-output stability
Notes: 4.1 Definitions of stability The most commonly used definitions of stability are based on the magnitude of the system response in the steady state. If the steady-state response is unbounded, the system is said to be unstable. In this lecture, we discuss two stability definitions that concern the boundedness or exponential decay of the system output. The first stability definition considers the system output due to its initial conditions. To apply it to transfer function models, we need the assumption that no pole-zero cancellation occurs in the transfer function.

## Slide 6: Asymptotic stability
Asymptotic stability: Response due to any initial conditions decays to zero asymptotically in the steady state
0
min
max

## Slide 7: Marginal stability
Marginal stability: response due to any initial conditions remains bounded but does not decay to zero
0
max

## Slide 8: Unstable stability
0
min
max

## Slide 9: Bounded-Input-Bounded-Output (BIBO) Stability
BIBO stability: Response due to any bounded input remains bounded
Notes: Input: u(k)
Output: y(k)

## Slide 10: Bounded-Input-Bounded-Output (BIBO) Stability
% MATLAB
close all, clear all, clc;
t = 0:3/60:3;
y =2*sin(2*pi*t);
y_add_offset = y+1;
stem(t,y_add_offset)
title('Bounded sequence with bound b_u=3');
xlabel('time (kT)');
ylabel('u(k)');
axis([0 3 -3 3]);

## Slide 11: Nội dung bài học
Khái niệm về tính ổn định
Mối quan hệ vị trí điểm cực và tính ổn định
Các điều kiện ổn định
Cách xác định tính ổn định hệ thống
Tiêu chuẩn ổn định Jury
Tiêu chuẩn ổn định Nyquist

## Slide 12
The sampled exponential and its z-transform
Time sequence for large k
Any time sequence
Stable z-domain pole locations (1)
(4.6)
Notes: The locations of the poles of the system z-transfer function determine the time response. The implications of this fact for system stability are now examined more closely

## Slide 13
Bounded sequence: if its poles lie in the closed unit disc (i.e., on or inside the unit circle) and decays exponentially if its poles lie in the open unit disc (i.e., inside the unit circle) due to any any bounded input remains bounded
Stable z-domain pole locations (2)
Image
z-plane
Stable
unstable
real
Notes: Note 1: Note that the case of repeated poles on the unit circle corresponds to an unbounded time sequence (see, for example, the transform of the sampled ramp)
Note 2: the preceding conclusion is valid for complex as well as real-time sequences, we will generally restrict our discussions to real-time sequences. For real-time sequences, the poles and partial fraction coefficients in Eq. (4.6) are either real or complex conjugate pairs.

## Slide 14: Nội dung bài học
Khái niệm về tính ổn định
Mối quan hệ vị trí điểm cực và tính ổn định
Các điều kiện ổn định
Cách xác định tính ổn định hệ thống
Tiêu chuẩn ổn định Jury
Tiêu chuẩn ổn định Nyquist

## Slide 15: Stability conditions
Asymptotic stability
BIBO stability
Internal stability
Notes: The derivation of conditions for asymptotic and BIBO stability based on transfer function models. It is shown that, in the absence of pole-zero cancellation, conditions for BIBO stability and asymptotic stability are identical

## Slide 16: Asymptotic stability (1)
Asymptotic stability: In the absence of pole-zero cancellation, an LTI digital system is asymptotically stable if its transfer function poles are in the open unit disc and marginally stable if the poles are in the closed unit disc with no repeated poles on the unit circle
Theorem 4.1
LTI system
Proof
Điều kiện ban đầu

## Slide 17: Asymptotic stability (2)
Proof
Using the z-transform of the output, we observe that the response of the system due to the initial conditions with the input zero
N(z) is a polynomial dependent on the initial conditions
+ transfer function zeros arise from transforming the input terms, they have no influence on the response due to the initial conditions
+ The denominator of the output z-transform is the same as the denominator of the z-transfer function in the absence of pole-zero cancellation
Hàm ảnh Y(z) có các đặc điểm sau:
+ the poles of the function Y(z) are the poles of the system transfer function
Notes: Theorem 4.1 applies even if pole-zero cancellation occurs, provided that the poles that cancel are stable. This follows from the fact that stability testing is essentially a search for unstable poles, with the system being declared stable if none are found. Invisible but stable poles would not lead us to a wrong conclusion. However, invisible but unstable poles would

## Slide 18: Asymptotic stability (3)
Examples
% Asymtotic Stablily
syms z;
%% Ha
Ha = 4*(z-2)/((z-2)*(z-0.1));
y = iztrans(Ha)
%% Hb
Hb = 4*(z-0.2)/((z-0.2)*(z-0.1));
y = iztrans(Hb)
%% Hc
Hc = 5*(z-0.3)/((z-0.2)*(z-0.1));
y = iztrans(Hc)
%% Hd
Hd = 8*(z-0.2)/((z-0.1)*(z-1));
y = iztrans(Hd)
The output due to the initial conditions is bounded for system poles in the closed unit disc with no repeated poles on the unit circle. It decays exponentially for system poles in the open unit disc (i.e., inside the unit circle)
Notes: Theorem 4.1 can only be used for transfer functions (a) and (b) if their poles and zeros are not canceled. Ignoring the zeros, which do not affect the response to the initial conditions, (a) has a pole outside the unit circle and the poles of (b) are inside the unit circle. Hence, (a) is unstable, whereas (b) is asymptotically stable.
Theorem 4.1 can be applied to the transfer functions (c) and (d). The poles of (c) are all inside the unit circle, and the system is therefore asymptotically stable. However, (d) has one pole on the unit circle and is only marginally stable

## Slide 19: BIBO stability
BIBO stability concerns the response of a system to a bounded input
The response of the system to any input is given by the convolution summation
h(k) - the impulse response sequence
(4.7)
Notes: Note: It may seem that a system should be BIBO stable if its impulse response is bounded. To show that this is generally false. Chứng minh ở slide kế tiếp (nếu thời gian cho phép) còn không, chỉ nói đến đây

## Slide 20: BIBO stability
Let the impulse response of a linear system be bounded and strictly positive with lower bound bh1 and upper bound bh2
Reapply to (4.7)
which is unbounded as k tiến đến vô cùng nếu tác động đầu vào là tín hiệu bị chặn được xác định như sau:
Notes: Chứng minh nhận định sai

## Slide 21: BIBO stability
A discrete-time linear system is BIBO stable if and only if its impulse response sequence is absolutely summabled, that is,
Theorem 4.2
Proof
1. Necessity (only if) To prove necessity by contradiction
2. Sufficiency (if) To prove sufficiency, we assume that (4.10) is satisfied and then show that
the system is BIBO stable
(4.10)
Notes: Điều kiện cần chứng minh bằng phản chứng
Điều kiện đủ chứng minh bằng logic
Có thời gian, chứng minh ở 2 slides kế tiếp

## Slide 22: BIBO stability
Proof
1. Necessity (only if) Ta chứng minh bằng phản chứng.
Giả sử hệ thống ổn định BIBO, song không thoả mãn (4.10)
Chọn tín hiệu đầu vào có dạng
The corresponding output is
which is unbounded as
Mâu thuẫn với giả thiết là hệ ổn định BIBO

## Slide 23: BIBO stability
Proof
2. Sufficiency (if) To prove sufficiency, we assume that (4.10) is satisfied and then show that the system is BIBO stable
the inequality
Rõ ràng ta thấy bị chặn.

## Slide 24: BIBO stability
A discrete-time linear system is BIBO stable if and only if the poles of its transfer function lie inside the unit circle
Theorem 4.3
Proof
Necessity (only if):
+the impulse response and transfer function shows that the impulse response is bounded if the poles of the transfer function are in the closed unit disc and decays exponentially if the poles are in the open unit disc.
+ It has already been established that systems with a bounded impulse response that does not decay exponentially are not BIBO stable. Thus, for BIBO stability, the system poles must lie inside the unit circle
Notes: Applying (4.6) to the impulse response and transfer function shows that the impulse response is bounded if the poles of the transfer function are in the closed unit disc and decays exponentially if the poles are in the open unit disc. It has already been established that systems with a bounded impulse response that does not decay exponentially are not BIBO stable. Thus, for BIBO stability, the system poles must lie inside the unit circle.

## Slide 25: BIBO stability
Proof
2. Sufficiency (if): assume an exponentially decaying impulse response (i.e., poles inside the unit circle). Let Ar be the coefficient of largest magnitude and |ps|<1 be the system pole of largest magnitude in (4.6). Then the impulse response (assuming no repeated poles for simplicity) is bounded by

## Slide 26: BIBO stability
Ví dụ 4.2: FIR
Investigate the BIBO stability of the class of systems with the impulse response
where K is a finite constant.
Solution
The impulse response satisfies
the systems are all BIBO stable
Notes: This is the class of finite impulse response (FIR) systems (i.e., systems whose impulse response is nonzero over a finite interval). Thus, we conclude that all FIR systems are BIBO stable

## Slide 27: BIBO stability
Ví dụ 4.3
Investigate the BIBO stability
Notes: + After pole-zero cancellation, the transfer functions (a) and (b) have all poles inside the unit circle and are therefore BIBO stable
+ The transfer function (c) has all poles inside the unit circle and is stable; (d) has a pole on the unit circle and is not BIBO stable

## Slide 28: BIBO stability
Kết luận
+ BIBO and asymptotic stability are equivalent and can be investigated using the same tests (no zero-pole cancelation)
Image
z-plane
Stable
unstable
real
Notes: The preceding analysis and examples show that for LTI systems, with no pole-zero cancellation, BIBO and asymptotic stability are equivalent and can be investigated using the same tests. Hence, the term stability is used in the sequel to denote either BIBO or asymptotic stability with the assumption of no unstable pole-zero cancellation. Pole locations for a stable system (inside the unit circle) are shown in Fig. 4.2.

## Slide 29: Internal stability
the stability of the closed-loop transfer function is not always sufficient for proper system operation because some of the internal variables may be unbounded
In a feedback control system, it is essential that all the signals in the loop be bounded when bounded exogenous inputs are applied to the system
+
-
+
+
Notes: + we have only considered stability as applied to an open-loop system. For closed-loop systems, these results are applicable to the closed-loop transfer function
+

## Slide 31: Internal stability
It is not sufficient to prove that the output of the controlled system Y is bounded for bounded reference input R because the controller output U can be unbounded.
The system output must be bounded when a different input is applied to the system namely, in the presence of a disturbance
+
-
+
+
Notes: + we have only considered stability as applied to an open-loop system. For closed-loop systems, these results are applicable to the closed-loop transfer function
+

## Slide 32: Internal stability
+
-
+
+
Notes: + we have only considered stability as applied to an open-loop system. For closed-loop systems, these results are applicable to the closed-loop transfer function
+

## Slide 33: Internal stability
The stability of the closed-loop transfer function is not always sufficient for proper system operation because some of the internal variables may be unbounded
In a feedback control system, it is essential that all the signals in the loop be bounded when bounded exogenous inputs are applied to the system
Internal stability: If all the transfer functions that relate system inputs (R and D) to the possible system outputs (Y and U) are BIBO stable, then the system is said to be internally stable.
Notes: + we have only considered stability as applied to an open-loop system. For closed-loop systems, these results are applicable to the closed-loop transfer function
+ In addition, the system output must be bounded when a different input is applied to the system - namely, in the presence of a disturbance

## Slide 34: Internal stability
The system is internally stable if and only if all its closed-loop poles are in the open unit disc.
Theorem 4.3
Proof
1. Necessity (only if)
we write C(z) and GZAS(z)
Notes: If the system is internally stable, then the four transfer functions in (4.11) have no poles on or outside the unit circle. Because of the factorization of (4.12) is coprime, the polynomial DCDG þ NCNG has no zeros that cancel with all four numerators. Thus, the polynomial has no zeros on or outside the unit circle

## Slide 35: Internal stability
The system is internally stable if and only if all its closed-loop poles are in the open unit disc.
Theorem 4.4
Proof
2. Sufficiency (if)
it is evident that if the characteristic polynomial DCDG and NCNG
has no zeros on or outside the unit circle, then all the transfer functions are asymptotically stable and the system is internally stable

## Slide 36: Internal stability
The system is internally stable if and only if all its closed-loop poles are in the open unit disc.
Theorem 4.4
Proof
2. Sufficiency (if)
it is evident that if the characteristic polynomial DCDG and NCNG
has no zeros on or outside the unit circle, then all the transfer functions are asymptotically stable and the system is internally stable

## Slide 37: Internal stability
The system is internally stable if and only if the following two conditions hold:
1. The characteristic polynomial 1 +C(z)GZAS(z) has no zeros on or outside the unit circle.
2. The loop gain C(z)GZAS(z) has no pole-zero cancellation on or outside the unit circle
Theorem 4.5
Proof
1. Necessity (only if)
2. Sufficiency (if)

## Slide 38: Internal stability
Necessity (only if)
+ Condition 1 is clearly necessary by Theorem 4.4.
+ Necessity of condition 2, (chứng minh phản chứng)
the characteristic polynomial
Proof

## Slide 39: Internal stability
Necessity (only if)
the characteristic polynomial
We assume that there exists which is a zero of DCDG as well as a zero of NCNG
Then clearly Z0 is also a zero of the characteristic polynomial DCDG +NCNG, and the system is unstable
This establishes the necessity of condition 2
Proof

## Slide 40: Internal stability
Sufficiency (if)
+ By Theorem 4.4, condition 1 implies internal stability unless unstable polezero cancellation occurs in the characteristic polynomial 1 + C(z)GZAS(z). We therefore have internal stability if condition 2 implies the absence of unstable pole-zero cancellation.
+ If the loop gain C(z)GZAS(z) =NCNG/DCDG has no unstable pole-zero cancellation, then 1+C(z)GZAS(z)=[DCDG + NCNG]/DCDG does not have unstable pole-zero cancellation, and the system is internally stable.
Proof

## Slide 41: Stability Condition
Example 4.3
1. Xác định GZAS(z) với T = 0.1
2. Kiểm tra tính ổn định internal stability của hệ thống

## Slide 42: Stability Condition
Example 4.3
1. Xác định GZAS(z) với T = 0.1
Condition 2 of Theory 4.5
Notes: + The system appears to be asymptotically stable with all its poles inside the unit circle + the system is not internally stable there is a pole of 1.334

## Slide 43: Nội dung bài học
Khái niệm về tính ổn định
Mối quan hệ vị trí điểm cực và tính ổn định
Các điều kiện ổn định
Cách xác định tính ổn định hệ thống

## Slide 44: Stability determination
Using Numerical Method ( MATLAB)
Tiêu chuẩn Routh-Hurwitz
Tiêu chuẩn Jury
Tiêu chuẩn Nyquist

## Slide 45: Using Numerical Method (MATLAB)
clear all, close all, clc
pole(gd); % if using transfer function
roots(gd.den); % using polynomial
abs(pole(gd) % Calculate magnitude of all roots
abs(roots(gd)) % Calculate magnitude of all roots

## Slide 46: Tiêu chuẩn Routh-Hurwitz
Phép biến đổi song tuyến tính
Tiêu chuẩn ổn định đại số (Routh_Hurwitz)

## Slide 47: Phép biến đổi song tuyến tính
The angle of w after bilinear transformation is
Notes: + the angle of w is of a magnitude greater than 90 degrees, which corresponds to points in the LHP
+ For a point on the unit circle, the angle is +, - 90 degrees, which corresponds to points on the imaginary axis
+ points outside the unit circle, the magnitude of the angle is less than 90 degrees, which corresponds to points in the RHP

## Slide 48: Tiêu chuẩn ổn định Routh-Hurwitz
For the general z-polynomial, we have the transform pair
Notes: The bilinear transformation allows the use of the Routh-Hurwitz criterion for the investigation of discrete-time system stability

## Slide 49: Tiêu chuẩn ổn định Routh-Hurwitz
The Routh-Hurwitz approach becomes progressively more difficult as the order of the z-polynomial increases
For high-order polynomials, a symbolic manipulation package can be used to perform the necessary algebraic manipulations
Notes: The bilinear transformation allows the use of the Routh-Hurwitz criterion for the investigation of discrete-time system stability

## Slide 50: Tiêu chuẩn ổn định Routh-Hurwitz
Ví dụ 4.5: Xác định tính ổn định
1. Đa thức bậc nhất
2. Đa thức bậc hai
1. Đa thức bậc nhất
2. Đa thức bậc hai
Lời giải: Tìm nghiệm của phương trình và xác định điều kiện để biên độ <1
Notes: + it is not easy to determine the stability of the second-order polynomial by solving for its roots.
+ Substituting the bilinear transformation in the second-order polynomial gives

## Slide 51: Tiêu chuẩn ổn định Routh-Hurwitz
Using bilinear transformation: for 2nd order equation
Apply Routh- Hurwitz for w
Notes: Without loss of generality, the coefficient a2 can be assumed to be unity, and the stable parameter range can be depicted in the a0 versus a1 parameter plane

## Slide 52: Tiêu chuẩn ổn định Jury
It is possible to investigate the stability of z-domain polynomials directly
  Jury test for real coefficients
  Schur-Cohn test for complex coefficients
The Jury test Procedure
The Jury test Procedure
Theorem 4.6
Notes: + These tests involve determinant evaluations as in the Routh-Hurwitz test for s-domain polynomials but are more time-consuming.
+ the roots of the polynomial are inside the unit circle if and only if (Jury)

## Slide 53: Jury Test Procedure
the roots of the polynomial are inside the unit circle if and only if

## Slide 54: Jury Test Procedure
Jury table

## Slide 55: Jury Test Procedure
The entries of the table are calculated as follows:

## Slide 56: Jury Test Procedure
The first row of the Jury table is a listing of the coefficients of the polynomial F(z) in order of increasing power of z.
The number of rows of table 2 n3 is always odd, and the coefficients of each even row are the same as the odd row directly above it with the order of the coefficients reversed
There are n + 1 conditions in (4.22) that correspond to the n+1 coefficients of F(z)
Condition 3 through n + 1 of (4.22) are calculated using the coefficient of the first column of the Jury table together with the last coefficient of the preceding row. The middle coefficient of the last row is never used and need not be calculated
Conditions 1 and 2 of (4.22) are calculated from F(z) directly. If one of the first two conditions is violated, we conclude that F(z) has roots on or outside the unit circle without the need to construct the Jury table or test the remaining conditions

## Slide 57: Jury Test Procedure
Condition 3 of (4.22), with an= 1, requires the constant term of the polynomial to be less than unity in magnitude. The constant term is simply the product of the roots and must be smaller than unity for all the roots to be inside the unit circle.
Condition (4.22) reduce to conditions (4.19) and (4.20) for first and second-order systems, respectively, where the Jury table is simply one row
For higher-order systems, applying the Jury test by hand is laborious, and it is preferable to test the stability of a polynomial F(z) using a computer-aided design (CAD) package
If the coefficients of the polynomial are functions of system parameters, the Jury test can be used to obtain the stable ranges of the system parameters

## Slide 58: Jury Test Procedure
Example 4.6

## Slide 59: Jury Test Procedure
Example 4.6
Notes: Conditions 2, 5, and 6 are violated, and the polynomial has roots on or outside the unit circle. In fact, the polynomial can be factored
+ a root at 2.5 outside the unit circle. Note that the number of conditions violated is not equal to the number of roots outside the unit circle and that condition 2 is sufficient to conclude the instability of F(z)

## Slide 60: Jury Test Procedure
Example 4.7
Find the stable range of the gain K for the unity feedback digital cruise control system
DAC and ADC if the sampling period is 0.02s
ZOH
T=.02
DAC
Plant
ADC
GZAS(z)
+
-
a. Find the transfer function for analog subsystem ADC and DAC
b. Find the stable range of the gain K
Notes: Y(z) ---- v(t)
E(z) ----- u(t)

## Slide 61: Jury Test Procedure
Example 4.7
a. The transfer function for analog subsystem ADC and DAC is
b. Find stable Range of K
clear all, close all, clc;
s = tf('s');
sys = K/(s+3);
T = 0.02;
sys_d = c2d(sys,T,'zoh')

## Slide 62: Jury Test Procedure
Example 4.8
Find the stable range of the gain K for the unity feedback digital cruise control system
DAC and ADC if the sampling period is 0.05s
ZOH
T=.05
DAC
Plant
ADC
GZAS(z)
+
-
a. Find the transfer function for analog subsystem ADC and DAC
b. Find the stable range of the gain K
Notes: Y(z) ---- y(t)
E(z) ----- u(t)

## Slide 63: Jury Test Procedure
Example 4.4
a. The transfer function for analog subsystem ADC and DAC is
clear all, close all, clc;
s = tf('s');
K=1
sys = 10*K/(s*(s+3));
T = 0.02;
sys_d = c2d(sys,T,'zoh')

## Slide 64: Jury Test Procedure
Example 4.8
b. Find stable Range of K

## Slide 65: Tiêu chuẩn Nyquist
The Nyquist criterion allows us to answer two questions:
1. Does the system have closed-loop poles outside the unit circle?
2. If the answer to the first question is yes, how many closed-loop poles are outside the unit circle?
The Nyquist criterion is particularly useful in situations where the frequency response can be obtained experimentally and used to obtain a polar or Nyquist plot.
The closed-loop characteristic polynomial
1. zeros of the pcl(z) are the closed-loop poles
2. poles of the pcl(z) are the open-loop poles
Notes: The Nyquist criterion allows us to answer two questions:
1. Does the system have closed-loop poles outside the unit circle?
2. If the answer to the first question is yes, how many closed-loop poles are outside the
unit circle?

## Slide 66: Tiêu chuẩn Nyquist
Problem Statement:
We assume that we are given the number of open-loop poles outside the unit circle (P). We need to find the number of closed-loop poles outside the unit circle (Z)
Nguyên lý góc quay
Tiêu chuẩn Nyquist
Phase and magnitude margin
Notes: To determine Z, we use some simple results from complex analysis. We first give the following definition.

## Slide 67: Nguyên lý góc quay
Contour: A contour is a closed directed simple (does not cross itself) curve
1. In the complex plane the vector connecting any point a to a point z is the vector (z-a)
2. The net angle change for the vector (z-a) as the point z traverses the contour in the shown (counterclockwise) direction by determining the net number of rotations of the corresponding vector
3. The point a1 - which is inside the contour- that the net rotation is one full turn (2π radians)
4. The point a2 - which is outside the contour- The net rotation is zero ( 0 radians)
5. If the point in question corresponds to a zero, then the rotation gives a numerator angle; if it is a pole, we have a denominator angle
Notes: The net angle change for a rational function is the change in the angle of the numerator minus the change in the angle of the denominator. So for Fig. 4.6, we have one counterclockwise rotation because of a1 and no rotation as a result of a2 for a net angle change of one counterclockwise rotation. Angles are typically measured in the counterclockwise direction and we count clockwise rotations as negative

## Slide 68: Nguyên lý góc quay
The net angle change for a rational function is the change in the angle of the numerator minus the change in the angle of the denominator
we have one counterclockwise rotation because of a1 and no rotation as a result of a2 for a net angle change of one counterclockwise rotation. Angles are typically measured in the counterclockwise direction and we count clockwise rotations as negative
Re-statements: how to determine the number of zeros of a rational function in a specific region; given the number of poles

## Slide 69: Nguyên lý góc quay
Select a closed contour surrounding the region.
Compute the net angle change for the function as we traverse the contour once.
The net angle change or number of counterclockwise rotations N is equal to the number of closed-loop poles inside the contour Zin minus the angle of open-loop poles inside the contour Pin, that is, the number of counterclockwise encirclements of the origin is given by

## Slide 70: Tiêu chuẩn ổn định Nyquist
To use this to determine closed-loop stability, we need to count the closed-loop poles outside the unit circle.(an nth order system)
The stability contour is the unit circle and is traversed in the counterclockwise direction

## Slide 71: Tiêu chuẩn ổn định Nyquist
The value of the loop gain on the unit circle is L(ejωT) (ωT = [-π,π])
Because the order of the numerator is equal to that of the denominator or less, points on the large circle map to zero or to a single constant value
Note that traversing the contour counterclockwise implies increasing ω and following the direction typically shown on Nyquist plots
We can simplify the test by plotting L(ejωT) as we traverse the contour and then counting its encirclements of the point (-1, j0)
Notes: +The values obtained for negative frequencies L(ejωT) are simply the complex conjugate of the values L(ejωT) and need not be separately calculated.
+ this is equivalent to plotting pcl(z) and counting encirclements of the origin (0,0)

## Slide 72: Tiêu chuẩn ổn định Nyquist
Let the number of counterclockwise encirclements of the point (1, j0) for a loop gain L(z) when traversing the stability contour be N (i.e., N for clockwise encirclements), where L(z) has P open-loop poles inside the contour. Then the system has Z closed-loop poles outside the unit circle with Z given by
Z = (-N) + P
Theorem 4.7
An open-loop stable system is closed-loop stable if and only if its Nyquist plot does not encircle the point (1, j0) (i.e., if N = 0)
Hệ quả

## Slide 73: Tiêu chuẩn ổn định Nyquist
Theorem 4.7
Although counting encirclements appears complicated, it is actually quite simple using the following recipe:
  Starting at a distant point, move toward the point (1, 0).
  Count all lines of the stability contour crossed. Count each line with an arrow pointing from your left to your right as negative and every line with an arrow pointing from your right to your left as positive.
  The net number of lines counted is equal to the number of clockwise encirclements of the point (1, 0).

## Slide 74: Tiêu chuẩn ổn định Nyquist
Special Case: Open-loop system has poles on unit Circle
=> the contour passes through poles and the test fails
We modify the contour to avoid these open-loop poles
The contour includes an additional circular arc of infinitesimal radius

## Slide 75: Tiêu chuẩn ổn định Nyquist
A net denominator angle change of mπ radians (counterclockwise) (i.e., m half circles). The net angle change for the quotient on traversing the small circular arc is thus mπ radians (clockwise). For a type m system, the Nyquist contour will include m large clockwise semicircles
The most common case is a pole at unity
The value of the transfer function on the circular arc is approximately given by
Notes: ε - là đường kính cung tròn, giá trị vô cùng bé

## Slide 76: Tiêu chuẩn ổn định Nyquist
Example 4.9
A linearized model of a furnace
In heating phase
ZOH
T=.01
DAC
Plant
ADC
GZAS(z)
+
-
clear all, close all, clc;
s = tf('s');
sys = 1/(s^2+3*s+1);
T = 0.01;
sys_d = c2d(sys,T,’zoh’)

## Slide 77: Tiêu chuẩn ổn định Nyquist
Example 4.9
nyquist(sys_d)
+ N = 0 - the Nyquist plot does not encircle the point (1, j0)
+ P = 0 - the open-loop transfer function has no unstable poles
Z = 0 - the system is closed-loop stable

## Slide 78: Tiêu chuẩn ổn định Nyquist
Example 4.10: The stability of the type-1 transfer function
clear all, close all, clc;
T = 0.01;
sys_d = tf(10,[1 -1.1 1],T)
nyquist(sys_d)
+ The Nyquist contour has two clockwise encirclements (N = -2)
Z = 2 - the system is closed-loop unstable

## Slide 79: Phase and Gain Margin
the stability of a mathematical model is not sufficient to guarantee acceptable system performance
We therefore need to determine how far the system is from instability. This degree of stability is known as relative stability
we restrict it to open-loop stable systems where zero encirclements guarantee stability. For open-loop stable systems that are nominally closed-loop stable, the distance from instability can be measured by the distance between the set of points of the Nyquist plot and the point (1, j0)
The distance = magnitude distance and angular distance
Notes: + In practice, the stability of a mathematical model is not sufficient to guarantee acceptable system performance or even to guarantee the stability of the physical system that the model represents
+ This is because of the approximate nature of mathematical models and our imperfect knowledge of the system parameters

## Slide 80: Phase and Gain margin
Gain margin: The gain margin is the gain perturbation that makes the system marginally stable.
Phase margin: The phase margin is the negative phase perturbation that makes the system marginally stable
+
-
Gain disturbance
Phase disturbance

## Slide 81: Phase and Gain Margin
The MATLAB commands for obtaining frequency response plots
nyquist(gd) % Nyquist Plot
bode(gd) % Bode Plot
On Nyquist and Bode plot, can select option
[GM, PM] = margin(gd); % find Margin
Gain and Phase margins

## Slide 82: Phase and Gain margin
Example 4.11
ZOH
T=.01
DAC
Plant
ADC
GZAS(z)
+
-
actuator
K

## Slide 83: Phase and Gain margin
Example 4.11
clear all; close all; clc;
T = 0.01;
z = tf('z',T);
Ga_d = 0.9516/(z-0.9048);
Gzas_d = 10^-5*(4.95*z+4.901)/(z^2-1.97*z+0.9704)
L_d = Ga_d*Gzas_d;
[GM,PM] = margin(L_d)
GM =
3.5699
PM =
46.3442

## Slide 84: Phase and Gain Margin
Example 4.12
Determine the closed-loop stability of the digital control system for the position control system with analog transfer function (T=0.01)

## Slide 85: Summary
Determine the input-output stability of a z-transfer function.
Determine the asymptotic stability of a z-transfer function.
Determine the internal stability of a digital feedback control system.
Determine the stability of a z-polynomial using the Routh-Hurwitz criterion.
Determine the stability of a z-polynomial using the Jury criterion.
Determine the stable range of a parameter for a z-polynomial.
Determine the closed-loop stability of a digital system using the Nyquist criterion.
Determine the gain margin and phase margin of a digital system.

## Slide 86: Quy ước về biểu diễn mã nguồn
int fact_do(int x)
{
int result = 1;
do {
result *= x;
x = x-1;
} while (x > 1);
return result;
}
int fact_goto(int x)
{
int result = 1;
loop:
result *= x;
x = x-1;
if (x > 1)
goto loop;
return result;
}
Phiên bản đầu tiên
Phiên bản thay thế
Mã nguồn được để trong ô có màu vàng, mã nguồn thay thế dược để trong ô màu xanh

## Slide 87: Nội dung bài học
Chủ đề 1
Chủ đề 2
Chủ đề 3
Chủ đề 4
Liệt kê nội dung, đến nội dung nào thì in đậm nội dung đó

## Slide 88
Section Template

## Slide 89: Mục đích, Yêu cầu
Mục đích
Yêu cầu
Mục đích, yêu cầu

## Slide 90: Nội dung chính
Chủ đề 1
Chủ đề 2
Chủ đề 3
Chủ đề 4
Liệt kê nội dung, đến nội dung nào thì in đậm nội dung đó

## Slide 91
Internal stability: If all the transfer functions that relate system inputs (R and D) to the possible system outputs (Y and U) are BIBO stable, then the system is said to be internally stable.C
Template cho khais nieemj

## Slide 92: Nội dung chính
Chủ đề 1
Chủ đề 2
Chủ đề 3
Chủ đề 4
Liệt kê nội dung, đến nội dung nào thì in đậm nội dung đó